## Slide 1: Maulana Azad National Institute of Technology, Bhopal
Line Following Robot with Obstacle Avoidance
Presented By -
Jatin Sharma ( 24216061101 )
Priyanshu Buwade ( 24216061108 )
Prashik Burbure ( 24216061112 )
Branch : Automation & Robotics
Subject : FAI-563 (SMES)
Guided By-
Dr. Vijay Bhaskar Semwal Assistant Professor(CSE),
MANIT Bhopal

## Slide 2: Contents
Introduction
Objective
Hardware Components Used
Circuit Diagrams
How Line Following Works
How Obstacle Avoidance Works
Flowchart
Code Overview
Challenges
Applications
Conclusions
References
i

## Slide 3: Introduction to Line Following & Obstacle Avoiding Robots
What is a Line Following Robot?
  A robot designed to follow a pre-defined path, typically a black line on a white surface.
  Uses Infrared sensors to detect and stay aligned with the path.
What is Obstacle Avoidance?
  Enables the robot to detect and bypass obstacles in its path using Ultrasonic sensor.
  Enhances the robot's capability to navigate dynamic environments.
1

## Slide 4: Objective
Combine line-following capability with obstacle avoidance to create an efficient and adaptive navigation system.
Implement real-time decision-making for handling obstacles while maintaining line-following accuracy.
2

## Slide 5: Hardware Components Used
Microcontroller
Arduino Uno is used as microcontroller.
Motors & Drivers
4 DC motors and L293D motors driver are used.
IR Sensors
To detect and follow the line.
Ultrasonic Sensor
To detect obstacle and avoid it.
Servo Motor
To adjust ultrasonic sensor's position for scanning.
Power Supply
To provide energy to the robot.
3

## Slide 6: Robot Circuit
4

## Slide 7: Circuit Diagram
5

## Slide 8: How Line Following Works
Basic Principle :
  Utilize infrared sensors to detect the line.
  Adjust movement based on sensor feedback to stay on course.
1. Following a Straight Line
6

## Slide 9: How Line Following Works
Basic Principle :
  Utilize infrared sensors to detect the line.
  Adjust movement based on sensor feedback to stay on course.
1. Following a Straight Line
6

## Slide 10: How Line Following Works
3. Following Right Curve
2. Following Left Curve
7

## Slide 11: How Line Following Works
3. Following Right Curve
2. Following Left Curve
7

## Slide 12: How Obstacle Avoidance Works
Basic Principle :
  Utilize ultrasonic sensor to detect the obstacle.
  Scan left and right using servo motor to detect obstacle on sides.
  Avoid obstacle by going from side with no other obstacle.
1. Detecting Obstacle and scanning sides
8

## Slide 13: How Obstacle Avoidance Works
Basic Principle :
  Utilize ultrasonic sensor to detect the obstacle.
  Scan left and right using servo motor to detect obstacle on sides.
  Avoid obstacle by going from side with no other obstacle.
1. Detecting Obstacle and scanning sides
8

## Slide 14: How Obstacle Avoidance Works
Basic Principle :
  Utilize ultrasonic sensor to detect the obstacle.
  Scan left and right using servo motor to detect obstacle on sides.
  Avoid obstacle by going from side with no other obstacle.
1. Detecting Obstacle and scanning sides
8

## Slide 15: How Obstacle Avoidance Works
2. Avoiding Obstacle
9

## Slide 16: How Obstacle Avoidance Works
2. Avoiding Obstacle
9

## Slide 17: How Obstacle Avoidance Works
2. Avoiding Obstacle
9

## Slide 18: How Obstacle Avoidance Works
2. Avoiding Obstacle
9

## Slide 19: How Obstacle Avoidance Works
2. Avoiding Obstacle
9

## Slide 20: Flowchart
10

## Slide 21: Code Overview
Code for Line Following
  if (leftSensor == LOW && rightSensor == LOW){
  moveForward(); // Both sensors detect the line
  }
  else if (leftSensor == HIGH && rightSensor == LOW) {
  turnRight(); // Left sensor off the line
  }
  else if (leftSensor == LOW && rightSensor == HIGH) {
  turnLeft(); // Right sensor off the line
  }
  else if (leftSensor == HIGH && rightSensor == HIGH) {
  releaseMotors(); // Both sensors off the line, stop
  }
11

## Slide 22: Code Overview
Code for Obstacle Avoidance
  if (distanceLeft > distanceRight) {
  turnLeft();
  delay(500);
  moveForward();
  delay(1000);
  turnRight();
  }
  else {
  turnRight();
  delay(500);
  moveForward();
  delay(1000);
  turnLeft();
  }
12

## Slide 23: Challenges
Coordination between Line Following & Obstacle Avoidance:
  Maintaining line detection during obstacle avoidance.
  Real-time obstacle detection and response.
Speed Control:
  Maintaining speed while ensuring accurate line following.
  Handling sharp turns, intersections, and obstacles.
Surface Variability:
  Different floor colours and textures can affect line detection.
13

## Slide 24: Applications
Industrial Automation
  Industrial automation for material handling.
  Transporting materials along predefined paths in factories.
In Hazardous environments
  Navigation in dynamic environments.
  Pathfinding in hazardous areas.
Education & Competitions
  Robotics competitions and educational projects.
  Participating in robotics contests to test design and coding skills.
14

## Slide 25: Conclusions
A line-following robot with obstacle avoidance demonstrates an advanced integration of sensor technology and control systems.
Offers a practical solution for autonomous navigation in dynamic environments.
Future scope includes AI integration for more complex decision-making.
Coordination between multiple robots for complex tasks.
15

## Slide 26: References
https://www.tinkercad.com/things/d4iIEqQIvXp-line-following-robot/
https://www.fypsolutions.com/robotics/line-following-algorithm-one-sensor/#google_vignette
https://marobotic.com/2023/10/22/line-follower-obstacle-avoiding-robot-using-arduino-and-l298-motor-driver/
https://www.instructables.com/Arduino-Obstacle-Avoidance-Line-Follower-Robot-Pro/
https://iarjset.com/wp-content/uploads/2023/06/IARJSET.2023.10670.pdf
https://www.youtube.com/watch?v=t7k9D1jDEtk&t=77s
https://www.youtube.com/watch?v=1n_KjpMfVT0
https://projecthub.arduino.cc/lightthedreams/line-following-robot-34b1d3
ii

## Slide 27
Thanks!